## Slide 1
EPSAC Rules

## Slide 2
Input
Ambient temperature
Discharge temperature
Process
Per day median of discharge temperature is calculated
Median ambient temperature + design limit temperature is taken as reference temperature
Output
1st alert will be triggered when median temperature > reference temperature for 48 Hrs
Compressor status
Median discharge temperature is compared with reference temperature
2nd alert will be triggered when median of next day is greater than or equal to previous day ( 24 Hrs )
3rd and 4th alert will triggered after 16 Hr & 8 Hr if median of discharge temperature is not reduced down
Design limit ( For high DOT considered as 65 C )
Day 1
Day 2
Day 3
Day 4
Day 5
Day 6
Day 7
Alert 1 in 48 Hr
2nd alert in next 24 Hr
3rd alert in next 16 Hr
4th alert in next 8 Hr
Reference Discharge temperature
Median Discharge temperature
Delta median Discharge temperature
Rule 1 : Median Discharge temperature > ( median ambient temperature + Design limit) for 48 Hr
Rule 2 : Median Discharge temperature > ( median ambient temperature + Design limit) AND > 90 C for 48 Hr
Rule 3 : Median Discharge temperature > 105 C for 48 Hr
Symptom 1: Compressor running with high discharge temperature

## Slide 3
Input
Compressor rated pressure ( Rated Pr )
Process
Case 1 : 100 % < compressor utilized < 120% , ( Rated Pr ) > Median Dis Pr > ( Rated Pr / 1.2 )
Output
If compressor operating continuously in case 1 mode for 3 months then alert will be triggered after 3 months
Discharge pressure ( Dis Pr )
Case 3 : compressor utilized > 140 %, Median Dis Pr < ( Rated Pr / 1.4 )
P1V1 = P2V2, Discharge pressure at 120 % of utilization = Rated Pressure / 1.2
For eg, If rated pressure of compressor is 7 bar, Discharge pressure at 120% utilization = 7/1.2 = 5.8 bar
Based on the median discharge pressure during load, compressor utilization mode is categorized
Case 2 : 120% < compressor utilized < 140 % , ( Rated Pr / 1.2 ) > Median Dis Pr > ( Rated Pr / 1.4 )
If compressor operating in case 2 mode for 48 Hrs. alert will be triggered.
If compressor is operating in case 3 mode for 24 Hrs. alert will be triggered.
Compressor running status ( Load / Unload )
120 %
100 %
140 %
Alert will be triggered after 3 months
Alert will be triggered after 48 Hrs
Alert will be triggered after 24 Hrs – 2 occurrence in a week
Rated Pressure
Rated Pressure / 1.2
Rated Pressure / 1.4
Compressor Utilization %
Median Discharge pressure
Alert will be triggered if there is 3 occurrence in 2 weeks
Alert will be triggered if there is 2 occurrence in 1 weeks
Symptoms 2 : Compressor running lower than set load pressure during load

## Slide 4
Rule condition :
Sump Pressure < 3.5 bar during load for 60 sec, alert will be triggered
Parameter | Intake valve | Solenoid valve | Blow down valve | Min. Pressure valve | Sump pressure bar.g
Case 1: Start (Runload) | Open | Open | Closed | Open | <3.5
Case 2: Noload to load | Open | Open | Closed | Open | <3.5
Proposed Method :
Air Alert rule :
Condition : If sump pressure < 0.3 (6sec) before star to delta
Information will be provided by neuron
Alert will be considered only if 2 out of 5 occurrence during star to delta ( This 5 occurrence will reset will there is trip in the machine )
Neuron trip :
Sump Pressure < 3.5 bar during load for 60 sec ( only during start )
Alert : If machine is in trip condition, for the same machine rule prediction alert will not be triggered.
Symptoms 3 : Compressor not loading

## Slide 5
Rule Condition : Load / unload count > design limit for last 48 Hrs ( > 20 load/unload per hour)
Proposed Condition :
Load/unload count – 1000 to 1500 / day for 15 occurrence / month
Load/unload count – 1500 to 3000 / day for 8 occurrence / 2 week
Load/unload count – > 3000/ day for 3 occurrence / 1 week
Symptoms 4 : More Number Of Load/Unload